PROPOSAL – 10/23/2023

PROJECT NAME AND ADDRESS:

LOS ANGELES LEADERSHIP ACADEMY

2670 GRIFFIN AVENUE, LOS ANGELES, CA 90031

Preparation:

- Protect all work areas as needed prior to commencement of work

Appliances:

- Imperial IR-10 Restaurant Series 60” wide Gas Range, Part # 27234

- Imperial ISB-36 Gas Salamander Broiler, 36” wide, Part # 16595

- Imperial Reinforced Channels to mount Salamander, Part # 31771

- Zephaire Convection Oven, Gas, 120K BTU, Part # 48210, Qty. 2

- Scotsman 15” wide Ice Machine, Built-in Pump, Part # SCCP50MB1SS

- DishStar HT-E Commercial Dishwasher, Part # 36257

Plumbing and Electrical Work:

- Perform rough plumbing and electrical work for the future installation of a commercial dishwasher

- Perform rough plumbing and electrical work for the future installation of an ice maker machine

- Perform rough plumbing and electrical work for the future installation of a stove

- Install the provided dishwasher, stove and icemaker

- Disconnect and remove an existing stainless steel sink; remove existing drains and water supply lines

- Install a new dedicated line with a separate breaker (240V–30AMP) and 30AMP outlet for the dishwasher

- Install a new dedicated line with a separate breaker (120V–20AMP) and 20AMP outlet for the icemaker

- Install a new dedicated line with a separate breaker (120V-15AMP) and 15AMP outlet for the stove

- Install new water supply and drain line pipes for the dishwasher and icemaker

- Connect and test the new stove, dishwasher, and icemaker.

**Materials in accordance to the specification stated above $61,491.88

** Sales Tax 5,841.73

**Labor in accordance to the specification stated above $10,450.00

Total project price including labor & materials: $77,783.61

Owner’s Signature  ____________________________  Date _________________________

Page 1

PROPOSAL – 10/23/2023

PROJECT NAME AND ADDRESS:

LOS ANGELES LEADERSHIP ACADEMY

2670 GRIFFIN AVENUE, LOS ANGELES, CA 90031

Schedule of payments:

Upon start of project				50%

Upon completion of plumbing and electrical work 	10%

Before appliance delivery				40%

All materials are guaranteed to be as specified. All work to be completed in a workmanlike manner according to standard practices. Any alterations or deviation from the above specifications involving extra costs will be executed only upon written orders and will become an extra charge over and above the estimate.

ACCEPTANCE OF PROPOSAL (TWO PAGES)

The above prices, specifications and conditions are hereby accepted. You are authorized to do the work as specified. Payments will be made as outlined above.

Accepted:

Date:	_____________________		Owner’s signature:  ____________________________